# Robot specifications:

- Max_Voltage = 9 V
- Max_Current = 86 mA
- Max_Power = 775 mW
- Wheel diameter = 30.4 mm
- Max RPM = 250
- Weight = 220 g (with batteries)
- Motors Speed at 50% = 146 RPM
# Robot requirements:

- Robot should have two “pillars”.
- The pillars are meant to identify the pose of the robot by the scanner.
- The robot should have a marker holder.
- The robot should draw a given path using the marker.
- Robot speed should be between 0.15 – 0.25 m/